# Construction of Prusa i3 by 3kd
- http://www.3kd.be/
- https://github.com/3000d/Prusa-i3
- http://d3000.dozuki.com/Guide/Guide+de+montage+-+Prusa+i3/3
- Photos of the workshop
## Howtos
Tips and tricks for 3D printing:
- Tips and tricks on perparing complex models for 3D printing
- Top 10 Tips for 3D Printing Design
- Prototypes That Last: Simple Tips for Making Durable Parts, Part 1
- Prototypes That Last: Simple Tips for Making Durable Parts, Part 2
- Resin Casting: Going from CAD to Engineering-Grade Plastic Parts
- 10 Tips For Modeling For 3D Printing
- Smoothing 3D printing with Acetone vapor bath
- Stress Testing Injected Hot Glue for Solid, Fast, Cheap 3D Prints
## Material
Extruder: 0.4mm or 400 micron
(Warning: When buying metal extruders. If there is no teflon tube inside, it will not work with PLA. It blocks when hot)
## Configuration of Slic3r
Layer height: never go over 80% of the extruder hardware value.
## Shops
http://reprap.me/
## Configuration
Here are some values for my Prusa i3kd. (I just keep them here to remember them)
Dimensions of the plateform:
- With (X): 185cm
- Length(Y): 170cm
- Height:(Z): 190cm
### Configuring the extruder motor
In pronteface.py: To get the values from the firmware, type
M501
Ex:
>>> M501
SENDING:M501
echo:Stored settings retrieved
echo:Steps per unit:
echo: M92 X80.00 Y80.00 Z4000.00 E765.00
echo:Maximum feedrates (mm/s):
echo: M203 X500.00 Y500.00 Z3.00 E25.00
echo:Maximum Acceleration (mm/s2):
echo: M201 X9000 Y9000 Z100 E10000
echo:Acceleration: S=acceleration, T=retract acceleration
echo: M204 S3000.00 T3000.00
echo:Advanced variables: S=Min feedrate (mm/s), T=Min travel feedrate (mm/s), B=minimum segment time (ms), X=maximum XY jerk (mm/s), Z=maximum Z jerk (mm/s), E=maximum E jerk (mm/s)
echo: M205 S0.00 T0.00 B20000 X20.00 Z0.40 E5.00
echo:Home offset (mm):
echo: M206 X0.00 Y0.00 Z0.00
echo:PID settings:
echo: M301 P22.20 I1.08 D114.00
Read the ligne that starts with M92 and write down the value from E###
Then use a ruler to mark 10 cm of filament and launch an extrusion of 10cm of filemant using pronterface. Then measure the actual amount of filament extruded.
(M92 E###) * ( 10cm / measured) = new value for M92
Enter this new value like this:
M92 E###
And save by typing this:
M500
Repeat 2 or 3 times to get the number right.
### Configure Slic3r settings
- filament diameter : measure it from the actual filament used (do multiple measures and average it)
- filament extrusion multiplier: to lower (<1) or raise (>1) the amount of filament extruded
### Printer settings
Use these values to play with the layers' heights for parts of the model (perimeter, fill,…)